## Slide 1
Investigating the dynamics of extreme wave energy transfer
during propagation towards coastal zones
Reine MATAR
24-27th of October 2023 Coast Caen
UNICAEN | Université de Caen Normandie
UMR CNRS 6143 "Morphodynamique Continentale et Côtière"
reine.matar@unicaen.fr
Nizar ABCHA, Imen TURKI, and Nicolas LECOQ

## Slide 2
Introduction
Literature Review
Objectives
Materials and methods
Results and discussion
Conclusion
Future directions
Q&A
GENERAL PLAN

## Slide 3
Introduction
On February 8, 2020, storm Ciara recorded a swell height greater than 4 m Causing a significant marine submersion of Etretat beach and that of Hautôt-sur-mer.
The Normandy coastline experiences severe hydrodynamic conditions, including powerful tidal currents, intense waves, and strong turbulence.
storm Ciara Etretat - Bing images

## Slide 4
    Gaps in the existing literature:
      Lack of Autobicoherence Analysis in Coastal Dynamics
      Limited Understanding of Energy Dissipation Mechanisms
      Incomplete Frequency Interaction Analysis
      Limited Application of Wavelet Transform in Coastal Studies
Studying the impact of extreme storm events on the hydro-morphodynamics in the coastal zone by physical modeling through wave flume experimentation.
Research Landscape and Literature Gap

## Slide 5
vague extreme Etretat - Bing images
Literature Review
Extreme events can be generated by many ways :
  Sudden variation in bathymetry
  Modulational instability (for kh > 1.36)
  Collision between two soliton
  Focused waves
Kharif et al., 2009
Touboul et al., 2015
Cavaleri et al. 2012
Benjamin et al., 1967
Marin, F. et al., 2005 a, b.

## Slide 6
= π
  Focused waves

## Slide 7
Gaussian
Pierson-Moskowitz
JONSWAP (γ=3.3)
JONSWAP (γ=7)
Spectra of Pierson-Moskowitz and JONSWAP
γ : correction factor
Gaussian envelope of a wave train (Günther. 1986.)
  Wave train spectra

## Slide 8
Uncover the hidden dynamics of coastal waves through advanced analysis techniques.
      Introduce autobicoherence analysis to coastal dynamics research.
      Investigate energy dissipation mechanisms during wave propagation.
      Explore nonlinear frequency interactions often overlooked.
      Utilize wavelet transform for identifying frequency components.
Objectives

## Slide 9
Materials and methods
Wave flume
L x l = 20 m x 0.8m
Inclined PVC beach β = 1/25
Water level h0 = 0.3 m
Wave Generator
Peak frequency = 0.75 Hz
9 wave amplitudes
Wave breaking at 12m from generator
4 spectra: Gaussian, Pierson-Moskowitz
JONSWAP (γ = 3,3) et JONSWAP (γ = 7)
Wave generator (done using Autocad by Sylvain Haquin)
Wave flume (done using Autocad by Sylvain Haquin)

## Slide 10
Spectrum
Jonswap (γ = 7)
Spectrum
Jonswap (γ = 3.3)
Spectrum
Pierson Moskowitz (γ = 1)
Spectrum
Gaussian
Wave Spectra used
Free surface elevation (m) versus time (s)
Power spectral density versus frequency (Hz)

## Slide 11
Number
1 wave train
Number
3 wave train
Number
6 wave trains
Number
9 wave trains
Wave train number used
Free surface elevation (m) versus time (s)

## Slide 12
Wave Gauges positions
Wave Gauges
51 Positions :
  WG1 4m (reference)
  Packet of 5 WG (x10)
Reference
signal
Wave breaking
Toe of slope
Sketch of the wave flume. The direction of propagation: from left to right

## Slide 13
 | JS 7 | JS 3.3 | PM | Gaussian
Peak frequency fp | 0.75 Hz | 0.75 Hz | 0.75 Hz | (0.5 - 1) Hz
Non-linearity S0 = Ks x | 0.21 0.27 0.34 0.41 0.49 0.58 0.65 0.70 0.72 | 0.21 0.26 0.31 0.38 0.44 0.51 0.58 0.66 0.74 | 0.19 0.24 0.29 0.35 0.40 0.46 0.52 0.58 0.65 | 0.10 0.13 0.16 0.19 0.23 0.26 0.30 0.34 0.38
Nb of Trains | 1 – 3 – 6 – 9 | 1 – 3 – 6 – 9 | 1 – 3 – 6 – 9 | 1 – 3 – 6 – 9
WG positions | 51 | 51 | 51 | 51
 | JS 7 | JS 3.3 | PM | Gaussian
Peak frequency fp | 0.75 Hz | 0.75 Hz | 0.75 Hz | (0.5 - 1) Hz
 | 0.21 0.27 0.34 0.41 0.49 0.58 0.65 0.70 0.72 | 0.21 0.26 0.31 0.38 0.44 0.51 0.58 0.66 0.74 | 0.19 0.24 0.29 0.35 0.40 0.46 0.52 0.58 0.65 | 0.10 0.13 0.16 0.19 0.23 0.26 0.30 0.34 0.38
Nb of Trains | 1 – 3 – 6 – 9 | 1 – 3 – 6 – 9 | 1 – 3 – 6 – 9 | 1 – 3 – 6 – 9
WG positions | 51 | 51 | 51 | 51
Flume experiments
1350 signals
Ks : Characteristic wavenumber
fs : Characteristic frequency
(2𝜋𝑓s)² = g 𝑘s tanh (𝑘sℎ0)
Dispersion relationship
Experiments summary

## Slide 14
b²(f1,f2) for a frequency triplet (f1, f2 et f1 + f2)
0: Non-existent interaction
1: Maximum interaction
Mother wavelet : Morlet
 | Linear theory | Non-linear theory
Frequencies Interaction | No | Yes
Analysis | Spectral : FFT | Bi-spectral : Bi-coherence
Processing techniques
Sinus FFT - Bing images

## Slide 15
Results and discussions
51 Positions :
  WG1 4m (reference)
  Packet of 5 WG (x10)
Reference
signal
Wave breaking
Toe of slope
Sketch of the wave flume. The direction of propagation: from left to right

## Slide 16
Power Spectral Density
Experimental Pierson-Moskowitz spectrum in different scales: (a) Spatial evolution of the spectrum; and (b) Spectra of three positions.
(a)
(b)

## Slide 17
Wave Energy differential:
Energy dissipation percentage using a Jonswap (γ =3.3) spectrum for multiple nonlinearities.

## Slide 18
Spatial evolution of auto-bicoherence for 6 different sections along the canal.
(a): x = -5.6m (h = 0.3 m), (b): x = -2.8 m (h = 0.3 m), (c): x = 0 m (h = 0.3 m), (d) : x = 2 m (h = 0.24 m), (e) : x = 2.4 m (h = 0.2 m), (f) : x = 4 m (h = 0.12 m)
Auto-bicoherence
(a)
(b)
(c)
(d)
(e)
(f)

## Slide 19
Frequency components (MODWT)
Free surface elevation (m) of the reference signal versus time (s)
Sketch of the wave flume. The first wave gauge is indicated (-5.6m)

## Slide 20
  Components signals (Initial position)
Data points
Data points
Data points

## Slide 21
Free surface elevation (m) of the final signal versus time (s)
Sketch of the wave flume. The last wave gauge is indicated (4.4m)

## Slide 22
Data points
Data points
  Components signals (Final position)
Data points

## Slide 23
  Energy
Frequency components
Spectrum: JS3.3 S0 = 0.74 Nb of Trains = 6
Frequency components energy versus WG positions (m)
d5
d4
d8

## Slide 24
  Energy differential ()
Wave breaking
Wave breaking
Frequency components
Frequency components energy differential versus WG positions (m)

## Slide 25
Conclusion
  Autobicoherence analysis unveiled intricate frequency interactions in coastal waves, suggesting a connection between these interactions and energy dissipation.
  Our exploration expanded with wavelet analysis, linking energy dissipation to specific frequency components.
Our work is a stepping stone toward safeguarding coastal regions in the face of evolving challenges.

## Slide 26
Future Directions
Wave statistics
PDF
Skewnes
Kurtosis
And higher order moments
Sediment Transport
Flume experiments
+ sediments
Numerical modeling
Digital Twin, Machine Learning
Results confirmation
mPeregrine
Boussinesq equations
Xbeach
Simulation of in situ data

## Slide 27
THANK YOU FOR YOUR ATTENTION
QUESTIONS ?

## Slide 28
(a)
(b)
(c)
(d)
(e)
(f)

## Slide 29
Wavelet transform
  Frequency components evolution

## Slide 30
d5
d8
Machine Learning
  Predicting frequency components energy

## Slide 31
Skewness
Kurtosis
Machine Learning
  Predicting Skewness and kurtosis